## Slide 1: Internet des objets et Contiki
Sébastien DAWANS
Laurent DERU
17/10/2013
© CETIC – www.cetic.be
Jeudis du Libre, UMons

## Slide 2
Embedded &
Communication Systems
Software & System Engineering
Software & Services Technologies

## Slide 3: Menu du jour
Définition de l’Internet des Objets
Standards de l’IoT
Contiki
Activités du CETIC

## Slide 4
RFID
1999
Internet of Things
200x
M2M
201x
Smartphones,
RFID, Cloud…
Junction of the physical and digital worlds

## Slide 5: Cisco’s Vision
Source: Cisco IBSG, April 2011
Birth of
the IoT

## Slide 6: « the * syndrome »
Any*
Smart*
AnyOne
AnyThing
AnyWhere
AnyBusiness
AnyNetwork
AnyContext
SmartHome
SmartBuilding
SmartEnergy
SmartGrid
SmartCity
SmartFactory
SmartAgriculture
*aware
Context-Aware
Self-Aware
Process-Aware
… ?

## Slide 8: Gartner, 2011

## Slide 9: Gartner, 2012

## Slide 10: Gartner, 2013

## Slide 11: IMHO… IoT is
Interacting with the
Physical World
using Software
and Networking

## Slide 12
Internet of Things
1: IPv6
Open Standard
Widespread
Scalable
Auto-configuration
Simple

## Slide 13: Contiki: OS for the IoT
Runs on small devices, sensor networks, etc
Low power, low memory
Certified IPv6 stack
Supports a variety of hardware
Open-source, contributors from
  SICS, Cisco, Redwire LLC, and many others

## Slide 14
Internet of Things
2: Cloud
Cloud-centric IoT
Objects as simple as possible
Intelligence in the Cloud
Standard interfaces
No complex application logic

## Slide 15: Cloud-Centric IoT
app
app
app
app
app

## Slide 16
Internet of Things
3: Semantics
Object identity
Virtual/Physical duality
Service & Role discovery
CoAP

## Slide 17: IoT will be based on semantics
GET <resource>
<of what?>
app
reply
POST <data>
<to what?>
app
app
PUSH
<notification>

## Slide 18
Some
Applications

## Slide 19: Smart Parking
Smart
Park
Cloud App:
APIs
Path Calculation
WSN Mngt
Billing
Keep objects and clients simple
http://www.libelium.com/smart_parking/

## Slide 20: Smart Grid
Clever electricity management
  Generation, distribution, consumption
  Green, efficient, secured
Dynamic pricing
Anticipation of needs

## Slide 21: Smart Grid in a Zoning

## Slide 22: Smart Grid in a Zoning
= €

## Slide 23
= €
Smart Grid in a Zoning

## Slide 24: Smart Grid in a Zoning
= €
Let’s optimize locally
Self-sufficiency

## Slide 25: Smart Grid in a Zoning
= €
-18°C
Zoning Optimizer
share energy
control
control

## Slide 26: Smart Grid in a Zoning
-24°C
= €
Zoning Optimizer
control
control
store energy

## Slide 27: Smart Grid in a Zoning
Zoning Optimizer
Inputs:
Production forecast
Consumption forecast
Urgency of tasks
Optimization Criteria
Outputs:
Schedule proposition
Announce supply/demand
Global optimization
  Instead of local optim.
Calculate « cost » of kWh

## Slide 28
Is one vision of the IoT
Inspired by the World Wide Web
Objects connect through the Web
Objects use Web protocols (& technologies & tools)
Adoption of the RESTful architecture

## Slide 29
Designing The
IoT

## Slide 30: Open Standards
What we already had
  IPv4/6
  A massive internet
  Isolated Wireless Sensor Networks (WSN)

## Slide 31: Wireless Sensor Networks (WSN)
Multihop
Autonomous
  Low-Power
  Low-Throughput
  No Maintenance
Fault-tolerant
Data-collect
Gateways
Traditionally:

## Slide 32: Wireless Sensor Networks (WSN)
Multihop
Data Collection
Common
Destination

## Slide 33: Typical WSN Hardware
µC
  8-16kB RAM, 48-128kB Flash
  A few MHz
802.15.4 radio
a few sensors
GPIO
Some external flash (1-8 Mbit)
Batteries
Cheap

## Slide 34: Wireless Sensor Networks (WSN)
Now becoming a subset of IoT
IoT
WSN
Bidirectionnal
Data Patterns
GET
IPv6
IPv6

## Slide 35: Wireless Sensor Networks (WSN)
Now becoming a subset of IoT
IoT
WSN
Bidirectionnal
Data Patterns
response
IPv6
IPv6

## Slide 36: Wireless Sensor Networks (WSN)
Now becoming a subset of IoT
IoT
WSN
Bidirectionnal
Data Patterns
response
Full end-to-end IPv6
IPv6
IPv6

## Slide 37: Open Standards
What we already had
  IPv4/6
  A massive internet
  Isolated Wireless Sensor Networks (WSN)
What was added (IETF)
  6LoWPAN: IPv6 for 802.15.4 WSNs
  RPL: Routing protocol for 6LoWPAN
  CoAP: RESTful protocol for constrained applications

## Slide 38: IPv6: the Narrow Waist
802.3x
802.15.4
IPv6
6LoWPAN
HTTP
CoAP
NDP
RPL

## Slide 39: IPv6: the Narrow Waist
802.3x
802.15.4
IPv6
6LoWPAN
HTTP
CoAP
NDP
RPL

## Slide 40: 6LoWPAN: IPv6 for 802.15.4
Maximum Transmission Unit (MTU)
  Minimum 1280 bytes in IPv6
  But Maximum 127 bytes MAC frames in 802.15.4
MAC 802.15.4
IPv6
UDP
DATA
~25 B
40 B
127 B
8 B
54 B
56% overhead
44% data

## Slide 41: 6LoWPAN: IPv6 for 802.15.4
Maximum Transmission Unit (MTU)
  Minimum 1280 bytes in IPv6
  But Maximum 127 bytes MAC frames in 802.15.4
6LoWPAN: Reduce the IPv6 packet size
  Header Compression
  Fragmentation
MAC 802.15.4
IPv6
UDP
40 B
127 B
8 B
54 B
56% overhead
44% data
~25 B
DATA

## Slide 42: 6LoWPAN Header Compression
Version
0
7
23
15
31
TC
Flow Label
Payload Length
Next Header
Hop Limit
Source Address (128 bits)
Destination Address (128 bits)
16 B
16 B
8 B
Goal: Compress as much of the IPv6 Header

## Slide 43: 6LoWPAN Header Compression
Goal: Compress as much of the IPv6 Header
Insert 6LoWPAN Header with compression information
3 mechanisms
  Make assumptions
  Infer Information from 802.15.4 Header
  Compress possible values to a subset
MAC 802.15.4
IPv6
UDP
DATA
6LoWPAN
« dispatch »

## Slide 44: 6LoWPAN Header Compression
Version
0
7
23
15
31
TC
Flow Label
Payload Length
Next Header
Hop Limit
Source Address (128 bits)
Destination Address (128 bits)
16 B
16 B
8 B
Always 6!
0 1 1
T F
NH
HLIM
CID
SAC
DAC
M
DAM
0 1 2 3 4 5 6 7 8 9 10 11 12 13 14 15
DAM
dispatch

## Slide 45: 6LoWPAN Header Compression
Version
0
7
23
15
31
TC
Flow Label
Payload Length
Next Header
Hop Limit
Source Address (128 bits)
Destination Address (128 bits)
16 B
16 B
8 B
Always 6!
Usually 0
0 1 1
T F
NH
HLIM
CID
SAC
DAC
M
DAM
0 1 2 3 4 5 6 7 8 9 10 11 12 13 14 15
DAM
4 possible states of TF: carried inline or not, etc
 Best case (11): assume all 0, save 3 bytes
dispatch

## Slide 46: 6LoWPAN Header Compression
Version
0
7
23
15
31
TC
Flow Label
Payload Length
Next Header
Hop Limit
Source Address (128 bits)
Destination Address (128 bits)
16 B
16 B
8 B
Always 6!
Usually 0
Inferred
0 1 1
T F
NH
HLIM
CID
SAC
DAC
M
DAM
0 1 2 3 4 5 6 7 8 9 10 11 12 13 14 15
DAM
dispatch

## Slide 47: 6LoWPAN Header Compression
Version
0
7
23
15
31
TC
Flow Label
Payload Length
Next Header
Hop Limit
Source Address (128 bits)
Destination Address (128 bits)
16 B
16 B
8 B
Always 6!
Usually 0
Inferred
subset
0 1 1
T F
HLIM
CID
SAC
DAC
M
DAM
0 1 2 3 4 5 6 7 8 9 10 11 12 13 14 15
DAM
NH
0: inline = 1 byte in IPv6 + next header inline
1: compressed = 1 byte defining NH + compression of next header
dispatch

## Slide 48: 6LoWPAN Header Compression
Version
0
7
23
15
31
TC
Flow Label
Payload Length
Next Header
Hop Limit
Source Address (128 bits)
Destination Address (128 bits)
16 B
16 B
8 B
Always 6!
Usually 0
Inferred
subset
0 1 1
T F
CID
SAC
DAC
M
DAM
0 1 2 3 4 5 6 7 8 9 10 11 12 13 14 15
DAM
NH
Inline; 1, 64, 255
subset
HLIM
dispatch

## Slide 49: 6LoWPAN Header Compression
Version
0
7
23
15
31
TC
Flow Label
Payload Length
Next Header
Hop Limit
Source Address (128 bits)
Destination Address (128 bits)
16 B
16 B
8 B
Always 6!
Usually 0
Inferred
subset
0 1 1
T F
CID
SAC
DAC
M
DAM
0 1 2 3 4 5 6 7 8 9 10 11 12 13 14 15
DAM
NH
Inline; 1, 64, 255
subset
HLIM
We need it for multihop
dispatch

## Slide 50: 6LoWPAN Header Compression
Version
0
7
23
15
31
TC
Flow Label
Payload Length
Next Header
Hop Limit
Source Address (128 bits)
Destination Address (128 bits)
16 B
16 B
8 B
Always 6!
Usually 0
Inferred
subset
0 1 1
T F
SAC
DAC
M
DAM
0 1 2 3 4 5 6 7 8 9 10 11 12 13 14 15
DAM
NH
subset
HLIM
CID
Most common: infer 64-bit prefix from link-local prefix
CID: stateful compression (more gain)
dispatch

## Slide 51: 6LoWPAN Header Compression
Result:
  IPv6 Header decreases from 40 bytes to about 7
  80-90 bytes for data
Fragmentation takes care of larger packets
  Fragmentation header with fragment ##

## Slide 52: More on 6LoWPAN
http://fr.wikipedia.org/wiki/6LoWPAN
Great Wikipedia Page in FR! (forget the EN one)
by Zach Shelby (Sensinode, ARM)
and Carsten Bormann (Universität Bremen)
by Adam Dunkels (SICS, Thingsquare)
and Jean-Philippe Vasseur (Cisco)
6LoWPAN: The Wireless Embedded Internet

## Slide 53: IPv6: the Narrow Waist
802.3x
802.15.4
IPv6
6LoWPAN
HTTP
CoAP
NDP
RPL

## Slide 54: RPL: Routing Protocol for 6LoWPAN
Facts
  Low Power & Lossy Networks (LLN)
  Links are highly dynamic
  Must support bidirectional traffic
    Optimized for collect (MP2P)
    Basic support of root  node (P2MP)
    Basic support of node  node (P2P)
  Energy / availability / latency compromise
    Must be flexible
  Scalable (destinations, density)

## Slide 55: RPL
DODAG: inspired by data-collect protocols
2
4
3
1
6
5
7

## Slide 56: RPL
DODAG: inspired by data-collect protocols
Periodic Broadcasts (DIO)
2
4
3
1
6
5
7

## Slide 57: RPL
DODAG: inspired by data-collect protocols
Periodic Broadcasts (DIO)
Uproutes
2
4
3
1
6
5
7

## Slide 58: RPL
DODAG: inspired by data-collect protocols
Periodic Broadcasts (DIO)
Uproutes
2
4
3
1
6
5
7

## Slide 59: RPL
DODAG: inspired by data-collect protocols
Periodic Broadcasts (DIO)
Uproutes
2
4
3
1
6
5
7

## Slide 60: RPL
DODAG: inspired by data-collect protocols
Periodic Broadcasts (DIO)
Uproutes
Keep broadcasting to
update ranks (with backoff)
2
4
3
1
6
5
7

## Slide 61: RPL
2
4
3
1
6
5
7
Periodic Broadcasts (DIO)
Uproutes
Keep broadcasting to
update ranks (with backoff)
Rank = cost to sink
Link
Metric
Link
Metric
Node
Metric
Rank 3, through 321 = Link 32 + Rank 2
Distance-vector routing protocol

## Slide 62: RPL
2
4
3
1
6
5
7
Periodic Broadcasts (DIO)
Uproutes
Keep broadcasting to
update ranks (with backoff)
Rank = cost to sink
Metric example: ETX, based
on dynamic measurements
Datapath Validation
ETX 2-1
ETX 3-2
Rank 3, through 321 = Link 32 + Rank 2
ETX: Estimated Transmission Count (Link metric)
 Cumulative TX to reach sink, through a parent

## Slide 63: RPL
2
4
3
1
6
5
7
Remember, IoT  Down Traffic
Down Traffic needs routing tables
PING 3
?

## Slide 64: RPL
2
4
3
1
6
5
7
Destination Advertisement
(DAO)
DAO: 3
DAO: 3,2
Remember, IoT  Down Traffic
Down Traffic needs routing tables

## Slide 65: RPL
2
4
3
1
6
5
7
Destination Advertisement
(DAO)
Dest | NH
3 | 3
Dest | NH
2 | 2
3 | 2
Remember, IoT  Down Traffic
Down Traffic needs routing tables

## Slide 66: RPL
2
4
3
1
6
5
7
Destination Advertisement
(DAO)
Dest | NH
3 | 3
Dest | NH
2 | 2
3 | 2
PING 3
Remember, IoT  Down Traffic
Down Traffic needs routing tables

## Slide 67: RPL
2
4
3
1
6
5
7
Destination Advertisement
(DAO)
Dest | NH
3 | 3
Dest | NH
2 | 2
3 | 2
PING 3
Remember, IoT  Down Traffic
Down Traffic needs routing tables
PING 3

## Slide 68: RPL
2
4
3
1
6
5
7
Destination Advertisement
(DAO)
Dest | NH
3 | 3
Dest | NH
2 | 2
3 | 2
PING 3
PING 3
PING 3
Remember, IoT  Down Traffic
Down Traffic needs routing tables

## Slide 69: RPL
2
4
3
1
6
5
7
P2P traffic is possible
Dest | NH
3 | 3

## Slide 70: RPL
2
4
3
1
6
5
7
P2P traffic is possible
Dest | NH
3 | 3
Dest | NH
2 | 2
3 | 2
7 | 6
… | 
5 | 2
Dest | NH
7 | 7

## Slide 71: IPv6: the Narrow Waist
802.3x
802.15.4
IPv6
6LoWPAN
HTTP
CoAP
NDP
RPL

## Slide 72: CoAP
A RESTful protocol
GET /temp
client
server
200 OK
app/text
23°C
client
server

## Slide 73: CoAP
http://fr.slideshare.net/zdshelby/coap-tutorial

## Slide 74: CoAP
http://fr.slideshare.net/zdshelby/coap-tutorial
CoAP: Time for a Demo

## Slide 75: Putting it all together
Contiki
www.contiki-os.org
www.github.com/contiki-os/contiki
802.3x
802.15.4
IPv6
6LoWPAN
HTTP
CoAP
NDP
RPL
with

## Slide 76: Contiki
2001
uIP
uIP:
TCP/IP stack for 8 & 16-bit µC
Single buffer
Standalone until v0.9
Tiny
  Code size < 5k
  RAM ~1k (= mostly the packet buffer)

## Slide 77: Contiki
2001
uIP
2003-2004
Contiki,
Protothreads

## Slide 78: Protothreads
Non pre-emptive systems
Event-Driven model (TinyOS)
  + Good for interfacing with hardware & reactive processing
  Difficult to sequence high-level operations, needs complex state machines
  Lots of functions  overhead
Protothreads (Contiki)
  + Linear code execution for event-driven systems
  + Low overhead (stackless threads)

## Slide 79: Protothreads: wait for events
int a_protothread(struct pt *pt) {
PT_BEGIN(pt);
PT_WAIT_UNTIL(pt, condition1);
if(something) {
PT_WAIT_UNTIL(pt, condition2);
}
PT_END(pt);
}
/* … */
/* … */
/* … */
/* … */
http://dunkels.com/adam/dunkels06protothreads.ppt ‎

## Slide 80: Protothreads: yielding
int a_protothread(struct pt *pt) {
PT_BEGIN(pt);
PT_WAIT_UNTIL(pt, condition1);
if(something) {
PT_WAIT_UNTIL(pt, condition2);
}
PT_END(pt);
}
int a_protothread(struct pt *pt) {
PT_BEGIN(pt);
PT_WAIT_UNTIL(pt, condition1);
if(something) {
PT_PAUSE(pt);
}
PT_END(pt);
}
SCHEDULER
int a_protothread(struct pt *pt) {
PT_BEGIN(pt);
PT_WAIT_UNTIL(pt, condition1);
if(something) {
PT_WAIT_UNTIL(pt, condition2);
}
PT_END(pt);
}
int a_protothread(struct pt *pt) {
PT_BEGIN(pt);
PT_WAIT_UNTIL(pt, condition1);
if(something) {
PT_WAIT_UNTIL(pt, condition2);
}
PT_END(pt);
}

## Slide 81: Protothreads
Bottom line
=
Let’s you program
sequentially with
multi-threading in C
On

## Slide 82: Contiki
2001
uIP
2003-2004
Contiki,
Protothreads
2007
COOJA,
Power Profiling

## Slide 83: COOJA
Run bytecode on
emulated HW
Time-accurate
WSN simulation

## Slide 84: Contiki
2001
uIP
2003-2004
Contiki,
Protothreads
2007
COOJA,
Power Profiling
2008
SICSLoWPAN

## Slide 85: Contiki
2001
uIP
2003-2004
Contiki,
Protothreads
2007
COOJA,
Power Profiling
2008
SICSLoWPAN
2009-2010
Many more
Platforms

## Slide 86: Multi-Platform Build System
User App
App-specific conf
Platform
Platform-specific conf
Contiki
Default
Conf
Contiki Modules & Applications
RPL
Coffee
Shell
Profiling
…

## Slide 87: Contiki
2001
uIP
2003-2004
Contiki,
Protothreads
2007
COOJA,
Power Profiling
2008
SICSLoWPAN
2009-2010
Many more
Platforms
2011
ContikiRPL
ContikiMAC

## Slide 88: ContikiMAC: Sleepy Radios
Radios are power-hungry
Current Draw of RX +/- same as TX
  ContikiMAC: Duty Cycle the Radio
  - Builds on previous RDC protocols
  - No synchronization
  - Supporting Async communications
  - < 1% Duty Cycle achieved
http://dunkels.com/adam/dunkels11contikimac.pdf

## Slide 89: ContikiMAC: Sleepy Radios
A
(sender)
B
(receiver)
~128 ms
Sleep, wake up periodically

## Slide 90: ContikiMAC: Sleepy Radios
A
(sender)
B
(receiver)
~128 ms
Unicasts: strobe until ACK’d
Start sending
at any time

## Slide 91: ContikiMAC: Sleepy Radios
A
(sender)
B
(receiver)
~128 ms
Unicasts: strobe until ACK’d
Data present,
It’s for me

## Slide 92: ContikiMAC: Sleepy Radios
A
(sender)
B
(receiver)
~128 ms
Unicasts: strobe until ACK’d
ACK
+
Back to sleep
ACK recv,
Stop sending

## Slide 93: ContikiMAC: Sleepy Radios
A
(sender)
B
(receiver)
Phase-Lock: anticipate wake-up by learning
ACK
+
Back to sleep
ACK recv,
Stop sending
Start slightly
earlier than
expected wake-up

## Slide 94: ContikiMAC: Sleepy Radios
A
(sender)
B
(receiver)
Phase-Lock: anticipate wake-up by learning
ACK
+
Back to sleep
ACK recv,
Stop sending
Start slightly
earlier than
expected wake-up
Saved power

## Slide 95: ContikiMAC: Sleepy Radios
A
(sender)
B
(receiver)
Broadcasts
~128 ms
>128 ms

## Slide 96: ContikiMAC
http://dunkels.com/adam/dunkels11contikimac.pdf

## Slide 97: Contiki
2001
uIP
2003-2004
Contiki,
Protothreads
2007
COOJA,
Power Profiling
2008
SICSLoWPAN
2009-2010
Many more
Platforms
2011
ContikiRPL
ContikiMAC
Connect to the Cloud: Thingsquare
2012

## Slide 98: Contiki-based Projects
www.tado.com
www.lifx.co
http://www.redwirellc.com/
Redwire self-powered sensor
http://www.noolitic.com/
http://www.dtectsystems.com

## Slide 99: Contiki
2001
uIP
2003-2004
Contiki,
Protothreads
2007
COOJA,
Power Profiling
2008
SICSLoWPAN
2009-2010
Many more
Platforms
2011
ContikiRPL
ContikiMAC
Connect to the Cloud: Thingsquare
2012
2013
6LBR

## Slide 100
Ongoing
Activities
@

## Slide 101: 6LBR: A Deployment-Ready Border Router for Internet of Things
Internet
WSN
CETIC (Laurent Deru, Sébastien Dawans)
UMons (Maxime Denis, Bruno Quoitin)

## Slide 102: 6LBR Overview
More info: https://github.com/cetic/6lbr/wiki/6LBR-Modes
Notes: sd

## Slide 103: 6LBR Features
Today
  Seamless integration of IPv6 and RPL
  Run smoothly on low-cost hardware
  Multi-BR (reliability, traffic balancing)
  Highly modular regression testing framework
Ongoing
  Multiple RPL Instances
  Expand user base
  Real-World Feedback

## Slide 104: 6LBR Demo

## Slide 105: 6LBR Test Framework
http://inl.info.ucl.ac.be/system/files/deru13redundant.pdf

## Slide 106: Multiple Border Routers
  Spatial Diversity, Redundancy…

## Slide 107: Multiple Border Routers
  Aggregate the WSN with external RPL Root

## Slide 108: Node Mobility

## Slide 109: Border Router Redundancy

## Slide 110: Network Partitioning

## Slide 111: 6LBR Platforms
RPi + Nooliberry
RPi + any « Contiki Mote »
BeagleBone
Econotag
BR12
Redwire, LLC

## Slide 113
Ongoing
Activities
@
IoT Testbed

## Slide 114: CETIC Testbed Deployment
25 nodes of 3 different models & border routers
6LBRs
Notes: mo & sd

## Slide 115: CETIC Testbed Overview
CETIC WSN Testbed
Server
SN1
SNn
…
Hub
Hub
Hub
Backend
USB Backbone
Web Frontend
Administration
Academic Experiments
IoT Products Prototyping
Control Jobs
Debug Info

## Slide 116: From Simulations to Reality
Simulation
Real World
Deployment
+ control
+ reproductibility
- poor channel models
- Limited hw platforms
- huge debugging issues
- physical access difficult
- many unexpected problems

## Slide 117: From Simulations to Reality
Simulation
Testbed
Real World
Deployment
+ control
+ reproductibility
- poor channel models
- Limited hw platforms
+ many platforms
+ near-real channel
- costly
- harder to debug
- huge debugging issues
- physical access difficult
- many unexpected problems

## Slide 118: From Simulations to Reality
Simulation
Testbed
Real World
Deployment
+ control
+ reproductibility
- poor channel models
- Limited hw platforms
+ many platforms
+ near-real channel
+ trace at every mote
- costly
- huge debugging issues
- physical access difficult
- many unexpected problems
Passive Sniffing
+ non-intrusive debugging
- partial information
- sniffer deployment

## Slide 119
Ongoing
Activities
Foren6
@
IoT Testbed

## Slide 120: Foren6: Passive IoT Diagnostics

## Slide 121: Still Alive? IoThanks!
sebastien.dawans@cetic.be
laurent.deru@cetic.be